## Slide 1: Industrial chemistry
Kazem.R.Abdollah
Polymers

## Slide 2: Introduction
Hermann Staudinger, a German chemist with experience in studying natural compounds such as rubber and cellulose. He formulated a polymeric structure for rubber, based on a repeating isoprene unit (referred to as a monomer). For his contributions to chemistry, Staudinger received the 1953 Nobel Prize.
Polymer: A polymer is a large molecule composed of many repeated subunits, known as monomers.
The terms polymer and monomer were derived from the Greek roots poly (many), mono (one) and meros (part).

## Slide 3: Writing Formulas for Polymeric Macromolecules

## Slide 4
Unlike simpler pure compounds, most polymers are not composed of identical molecules.
Two experimentally determined values are common:
Mn , the number average molecular weight, is calculated from the mole fraction distribution of different sized molecules in a sample.
Mw , the weight average molecular weight, is calculated from the weight fraction distribution of different sized molecules.

## Slide 5
Some Common Addition Polymers |  |  |  | 
Name(s) | Formula | Monomer | Properties | Uses
Polyethylene low density (LDPE) | –(CH2-CH2)n– | ethylene CH2=CH2 | soft, waxy solid | film wrap, plastic bags
Polyethylene high density (HDPE) | –(CH2-CH2)n– | ethylene CH2=CH2 | rigid, translucent solid | electrical insulation bottles, toys
Polypropylene (PP) different grades | –[CH2-CH(CH3)]n– | propylene CH2=CHCH3 | atactic: soft, elastic solid isotactic: hard, strong solid | similar to LDPE carpet, upholstery
Poly(vinyl chloride) (PVC) | –(CH2-CHCl)n– | vinyl chloride CH2=CHCl | strong rigid solid | pipes, siding, flooring
Poly(vinylidene chloride) (Saran A) | –(CH2-CCl2)n– | vinylidene chloride CH2=CCl2 | dense, high-melting solid | seat covers, films
Polystyrene (PS) | –[CH2-CH(C6H5)]n– | styrene CH2=CHC6H5 | hard, rigid, clear solid soluble in organic solvents | toys, cabinets packaging (foamed)
Polyacrylonitrile (PAN, Orlon, Acrilan) | –(CH2-CHCN)n– | acrylonitrile CH2=CHCN | high-melting solid soluble in organic solvents | rugs, blankets clothing
Polytetrafluoroethylene (PTFE, Teflon) | –(CF2-CF2)n– | tetrafluoroethylene CF2=CF2 | resistant, smooth solid | non-stick surfaces electrical insulation
Poly(methyl methacrylate) (PMMA, Lucite, Plexiglas) | –[CH2-C(CH3)CO2CH3]n– | methyl methacrylate CH2=C(CH3)CO2CH3 | hard, transparent solid | lighting covers, signs skylights
Poly(vinyl acetate) (PVAc) | –(CH2-CHOCOCH3)n– | vinyl acetate CH2=CHOCOCH3 | soft, sticky solid | latex paints, adhesives
cis-Polyisoprene natural rubber | –[CH2-CH=C(CH3)-CH2]n– | isoprene CH2=CH-C(CH3)=CH2 | soft, sticky solid | requires vulcanization for practical use
Polychloroprene (cis + trans) (Neoprene) | –[CH2-CH=CCl-CH2]n– | chloroprene CH2=CH-CCl=CH2 | tough, rubbery solid | synthetic rubber oil resistant

## Slide 6: Properties of Macromolecules
HDPE is a rigid translucent solid which softens on heating above 100ºC, and can be fashioned into various forms including films. It is not as easily stretched and deformed as is LDPE. HDPE is insoluble in water and most organic solvents, although some swelling may occur on immersion in the latter. HDPE is an excellent electrical insulator.
LDPE is a soft translucent solid which deforms badly above 75º C. Films made from LDPE stretch easily and are commonly used for wrapping. LDPE is insoluble in water, but softens and swells on exposure to hydrocarbon solvents.
Both LDPE and HDPE become brittle at very low temperatures (below -80º C). Ethylene, the common monomer for these polymers, is a low boiling ( – 104º C) gas.

## Slide 7
Because polymer molecules are so large, they generally pack together in a non-uniform fashion, with ordered or crystalline-like regions mixed together with disordered or amorphous domains.
Crystallinity occurs when linear polymer chains are structurally oriented in a uniform three-dimensional matrix. In the diagram on the right, crystalline domains are colored blue.
Increased crystallinity is associated with an increase in rigidity, tensile strength and opacity (due to light scattering).
crystalline domains are colored blue

## Slide 8
Three factors that influence the degree of crystallinity are:
  Chain length
  Chain branching
  Interchain bonding
  HDPE is composed of very long unbranched hydrocarbon chains. These pack together easily in crystalline domains that alternate with amorphous segments, and the resulting material, while relatively strong and stiff, retains a degree of flexibility.
  LDPE is composed of smaller and more highly branched chains which do not easily adopt crystalline structures. This material is therefore softer, weaker, less dense and more easily deformed than HDPE.

## Slide 9: 3.Interchain bonding
  The nature of cellulose supports the above analysis and demonstrates the importance of the third factor ( 3 ). These molecules align themselves side by side into fibers that are stabilized by inter-chain hydrogen bonding between the three hydroxyl groups on each monomer unit. Consequently, crystallinity is high and the cellulose molecules do not move or slip relative to each other. The high concentration of hydroxyl groups also accounts for the facile absorption of water that is characteristic of cotton.

## Slide 10
On heating or cooling most polymers undergo thermal transitions that provide insight into their morphology. These are defined as the melt transition, Tm , and the glass transition, Tg .
  Tm is the temperature at which crystalline domains lose their structure, or melt. As crystallinity increases, so does Tm.
  T g is the temperature below which amorphous domains lose the structural mobility of the polymer chains and become rigid glasses.

## Slide 11
Tm and Tg values for some common addition polymers are listed below.
Note that cellulose has neither a Tm nor a Tg.
Rubber is a member of an important group of polymers called elastomers. Elastomers are amorphous polymers that have the ability to stretch and then return to their original shape at temperatures above Tg. This property is important in applications such as gaskets and O-rings.
Polymer | LDPE | HDPE | PP | PVC | PS | PAN | PTFE | PMMA | Rubber
Tm (ºC) | 110 | 130 | 175 | 180 | 175 | >200 | 330 | 180 | 30
Tg (ºC) | _110 | _100 | _10 | 80 | 90 | 95 | _110 | 105 | _70

## Slide 12: Regio and Stereoisomerization in Macromolecules
Monosubstituted monomers, on the other hand, may join together in two organized ways, described in the following diagram.

## Slide 13
If the polymer chain is drawn in a zig-zag fashion, as shown above, each of the substituent groups (Z) will necessarily be located above or below the plane defined by the carbon chain. Consequently we can identify three configurational isomers of such polymers.
If all the substituents lie on one side of the chain the configuration is called isotactic.
If the substituents alternate from one side to another in a regular manner the configuration is termed syndiotactic.
Finally, a random arrangement of substituent groups is referred to as atactic.

## Slide 14: Synthesis of Addition Polymers
The most common and thermodynamically favored chemical transformations of alkenes are addition reactions.
Many of these addition reactions are known to proceed in a stepwise fashion by way of reactive intermediates, and this is the mechanism followed by most polymerizations.
A general diagram illustrating this assembly of linear macromolecules, are supports the name chain growth polymers.

## Slide 15
It is useful to distinguish four polymerization procedures fitting this general description.
  Radical Polymerization The initiator is a radical, and the propagating site of reactivity (*) is a carbon radical.
  Cationic Polymerization The initiator is an acid, and the propagating site of reactivity (*) is a carbocation.
  Anionic Polymerization The initiator is a nucleophile, and the propagating site of reactivity (*) is a carbanion.
  Coordination Catalytic Polymerization The initiator is a transition metal complex, and the propagating site of reactivity (*) is a terminal catalytic complex.

## Slide 16: 1. Radical Chain-Growth Polymerization
radical polymerization can be initiated by traces of oxygen or other minor impurities, pure samples of these compounds are often "stabilized" by small amounts of radical inhibitors to avoid unwanted reaction.
When radical polymerization is desired, it must be started by using a radical initiator, such as a peroxide or certain azo compounds.

## Slide 17
One example of this radical polymerization is the conversion of styrene to polystyrene.
The first two equations illustrate the initiation process, and the last two equations are examples of chain propagation.

## Slide 18
The most common termination processes are Radical Combination and Disproportionation.

## Slide 19
Chain transfer
This reaction moves a carbon radical from one location to another by an intermolecular or intramolecular hydrogen atom transfer (colored green).

## Slide 20: 2. Cationic Chain-Growth Polymerization
Polymerization of isobutylene (2-methylpropene) by traces of strong acids is an example of cationic polymerization.
Chain growth ceases when the terminal carbocation combines with a nucleophile or loses a proton, giving a terminal alkene (as shown here).

## Slide 21: 3. Anionic Chain-Growth Polymerization
Treatment of a cold THF solution of styrene with 0.001 equivalents of n-butyllithium causes an immediate polymerization. This is an example of anionic polymerization.
Only monomers having anion stabilizing substituents, such as phenyl, cyano or carbonyl are good substrates for this polymerization technique. Many of the resulting polymers are largely isotactic in configuration, and have high degrees of crystallinity.

## Slide 22: 4. Ziegler-Natta Catalytic Polymerization
An efficient and stereospecific catalytic polymerization procedure was developed by Karl Ziegler (Germany) and Giulio Natta (Italy) in the 1950's.
Ziegler-Natta catalysts are prepared by reacting certain transition metal halides with organometallic reagents such as alkyl aluminum, lithium and zinc reagents.
The catalyst formed by reaction of triethylaluminum with titanium tetrachloride has been widely studied, but other metals (e.g. V & Zr) have also proven effective.

## Slide 23
Polymerization of propylene through action of the titanium catalyst gives an isotactic product; whereas, a vanadium based catalyst gives a syndiotactic product.

## Slide 24: Copolymers
The synthesis of macromolecules composed of more than one monomeric repeating unit has been explored as a means of controlling the properties of the resulting material.
In this respect, it is useful to distinguish several ways in which different monomeric units might be incorporated in a polymeric molecule.

## Slide 25
The following examples refer to a two component system, in which one monomer is designated A and the other B.
Statistical Copolymers | Also called random copolymers. Here the monomeric units are distributed randomly, and sometimes unevenly, in the polymer chain: ~ABBAAABAABBBABAABA~.
Alternating Copolymers | Here the monomeric units are distributed in a regular alternating fashion, with nearly equimolar amounts of each in the chain: ~ABABABABABABABAB~.
Block Copolymers | Instead of a mixed distribution of monomeric units, a long sequence or block of one monomer is joined to a block of the second monomer: ~AAAAA-BBBBBBB~AAAAAAA~BBB~.
Graft Copolymers | As the name suggests, side chains of a given monomer are attached to the main chain of the second monomer: ~AAAAAAA(BBBBBBB~)AAAAAAA(BBBB~)AAA~.

## Slide 26: Addition Copolymerization
Most direct copolymerizations of equimolar mixtures of different monomers give statistical copolymers.
The copolymerization of styrene with methyl methacrylate, for example, proceeds differently depending on the mechanism:
Radical polymerization gives a statistical copolymer.
However, the product of cationic polymerization is largely polystyrene, and anionic polymerization favors formation of poly (methyl methacrylate).

## Slide 27
Formation of alternating copolymers is favored when the monomers have different polar substituents (e.g. one electron withdrawing and the other electron donating), and both have similar reactivities toward radicals. For example, styrene and acrylonitrile copolymerize in a largely alternating fashion.
A terpolymer of acrylonitrile, butadiene and styrene, called ABS rubber, is used for high-impact containers, pipes and gaskets
.
Some Useful Copolymers |  |  | 
Monomer A | Monomer B | Copolymer | Uses
H2C=CHCl | H2C=CCl2 | Saran | films & fibers
H2C=CHC6H5 | H2C=C-CH=CH2 | SBR styrene butadiene rubber | tires
H2C=CHCN | H2C=C-CH=CH2 | Nitrile Rubber | Adhesives hoses
H2C=C(CH3)2 | H2C=C-CH=CH2 | Butyl Rubber | inner tubes
F2C=CF(CF3) | H2C=CHF | Viton | gaskets

## Slide 28: Block Copolymerization
In the anionic polymerization of styrene described above, a reactive site remains at the end of the chain until it is quenched. The unquenched polymer has been termed a living polymer, and if additional styrene or a different suitable monomer is added a block polymer will form. This is illustrated for methyl methacrylate in the following diagram.

## Slide 29: Condensation Polymers
These polymerizations often (but not always) occur with loss of a small byproduct, such as water, and generally (but not always) combine two different components in an alternating structure. The polyester Dacron and the polyamide Nylon 66, shown here, are two examples of synthetic condensation polymers, also known as step-growth polymers.
In contrast to chain-growth polymers, most of which grow by carbon-carbon bond formation, step-growth polymers generally grow by carbon-heteroatom bond formation (C-O & C-N in Dacron & Nylon respectively).

## Slide 31: 1. Characteristics of Condensation Polymers
Condensation polymers form more slowly than addition polymers, often requiring heat, and they are generally lower in molecular weight.
The terminal functional groups on a chain remain active, so that groups of shorter chains combine into longer chains in the late stages of polymerization.

## Slide 32
The presence of polar functional groups on the chains often enhances chain-chain attractions, particularly if these involve hydrogen bonding, and thereby crystallinity and tensile strength.

## Slide 33
Some Condensation Polymers |  |  |  | 
Formula | Type | Components | Tg ºC | Tm ºC
~[CO(CH2)4CO-OCH2CH2O]n~ | polyester | HO2C-(CH2)4-CO2H HO-CH2CH2-OH | < 0 | 50
 | polyester Dacron Mylar | para HO2C-C6H4-CO2H HO-CH2CH2-OH | 70 | 265
 | polyester | meta HO2C-C6H4-CO2H HO-CH2CH2-OH | 50 | 240
 | polycarbonate Lexan | (HO-C6H4-)2C(CH3)2 (Bisphenol A) X2C=O (X = OCH3 or Cl) | 150 | 267
~[CO(CH2)4CO-NH(CH2)6NH]n~ | polyamide Nylon 66 | HO2C-(CH2)4-CO2H H2N-(CH2)6-NH2 | 45 | 265
~[CO(CH2)5NH]n~ | polyamide Nylon 6 Perlon |  | 53 | 223

## Slide 34: 2. Thermosetting vs. Thermoplastic Polymers
Most of the polymers described above are classified as thermoplastic. This reflects the fact that above Tg they may be shaped or pressed into molds, spun or cast from melts or dissolved in suitable solvents for later fashioning.
Another group of polymers, characterized by a high degree of cross-linking, resist deformation and solution once their final morphology is achieved. Such polymers are usually prepared in molds that yield the desired object. Because these polymers, once formed, cannot be reshaped by heating, they are called thermosets .